## Slide 1: Surface Ozone at different sites in the Tibetan Plateau (TP): Variations, Comparisons, and Implications
Lin Weili,
linwl@camscma.cn
Centre for Atmosphere Watch And Services
Meteorological Observation Centre
China Meteorological Administration

## Slide 2: Ozone observation in Tibetan Plateau (TP)
sea level
1000m
2000m
3000m
4000m
5000m
6000-
Huge Area (2,500,000 km2)
High average altitude (>4000 m)
Remote and Clean
Important snow cover in North Hemisphere
Strong solar radiation
Tibetan Plateau

## Slide 3: Surface ozone datasets (>1year)
Waliguan, 3800 m a.s.l., 1994-2015
Xianggelila, 3600 m a.s.l., 2004-2005, 2008-2015
Linzhi 3000 m a.s.l., 2014-2015
Lhasa urban city, 3650 m a.s.l., 2012-2015
Nam Co lake,4750 m a.s.l., 2011-2012
Dangxiong,4200 m a.s.l., 2009-2011

## Slide 4: Seasonal variations of ozone at different sites in the Tibetan plateau
Spring O3 maximum phenomena in the Northern Hemisphere
Asian monsoon season
Month

## Slide 5: O3 mixing ratio increase with the increase of altitude
汤洁等，2002

## Slide 6: NMC(30.77oN,90.96oE, 4748m )
DX (30.48oN, 91.10oE, 4187m)
Nam Co Lake
Nyainqêntanglha Mountains

## Slide 7: Comparison of O3 variations between DX and NMC
Similar day-to-day and week-to-week temporal fluctuations suggest that the sites are experiencing the same regional-scale background patterns in air quality and meteorology.
O3-NMC = (1.02±0.04)*O3-DX + (11.3±1.7), (R2=0.83, P<0.0001)

## Slide 8: Diurnal variations of O3 at NMC and Mixing layer height at a nearby site Naqu (~50km away)
Mixing height data from Dr. He Qianshan
Vertical mixing associated with surface strong wind speeds

## Slide 9: Relationships between surface O3 and wind speeds at DangXiong (DX)

## Slide 10: Similar diurnal change of O3 and wind speed at Xianggelila (XGLL)

## Slide 11: Surface O3 at TP has more features of free atmosphere
The diurnal ozone pattern seems very similar with the typical diurnal O3 pattern in urban or polluted area, at which photochemical product of O3 can accumulated after the noon.
The peak O3 at daytime is strongly associated with the wind speed and the mixing layer height.
Strong wind speed may destroy the photochemical accumulation of O3, in the clean remote area.
Therefore, the transport and deposition will be the key factors than the local photochemical process influencing the diurnal variations of surface O3 at the remote and clean sites at the Tibetan plateau.

## Slide 12: Long-term surface ozone trend?

## Slide 13
WLG: 3800 m a.s.l., 1994-2015
Xianggelila: 3600 m a.s.l., 2004-2005, 2008-2015

## Slide 14: Surface O3 trend at Xianggelila site

## Slide 15: Surface O3 trend at Waliguan site

## Slide 16: Similar long-term trends between WLG and XGLL
Waliguan: +0.25 ppb/yr
Xianggelila: +0.20 ppb/yr
(36.28◦N, 100.90◦E, 3810 m a.s.l.)
(28.006 N, 99.726 E; 3580ma.s.l.)

## Slide 17: How about the long-term change of surface ozone at urban city in TP
Such as Lhasa city? When it is
Under the strong solar (UV) radiation, and
A quick expansion of urban area with a factor of 10 since 1949;
An increase of tourist people about 200,000 in 1998 to 6,500,000 in 2012;
An increase of vehicle from 10,000 in 1998 to more than 150,000 in 2012;
GDP of 2.9 billion RMB in 1998, and 26.2 billion RMB in 2012.

## Slide 18
Observation site
Lhasa surface O3 measurement
Lhasa urban city: 3650 m a.s.l., June-August, 1998; 2012-2015

## Slide 19: Summer data in 1998 vs. in 2012
Impact of rapid urbanization on air pollution in Lhasa

## Slide 20: In 1998,
汤洁等，2002

## Slide 21: From 1998 to 2012, O3 behavior has change a lot at urban Lasa
1998
2012-2014

## Slide 22: Frequently occurring of high spikes of O3
(5-min time resolution data)
STE? No!
Highly spatial inhomogeneity in air pollution

## Slide 23: Summary
Surface ozone at TP has a more feature of free atmosphere.
Surface ozone has an increasing trend of more than 2ppb/10yr both at WLG and XGLL .
Surface ozone in summer at Lhasa urban city has an extreme increase (>10ppb) in the afternoon when compared with those in 1998, and it may be due to the significant increase of precursor emission under strong solar radiation.
In cold season, ozone spikes in Lhasa are more frequent than that in warm season, with a potential for winter photochemical pollution.

## Slide 24: Publications
W. Y. Xu, W. L. Lin, X. B. Xu*, J. Tang, J. Q. Huang, H. Wu, and X. C. Zhang. Long-term trends of surface ozone and its influencing factors at the Mt. Waliguan GAW station, China – Part 1: Overall trends and characteristics. Atmos. Chem. Phys. Discuss., 15, 30987-31024, doi:10.5194/acpd-15-30987-2015, 2015.
Ma, J., Lin, W. L.*, Zheng, X. D., Xu, X. B., Li, Z., and Yang, L. L: Influence of air mass downward transport on the variability of surface ozone at Xianggelila Regional Atmosphere Background Station, southwest China, Atmos. Chem. Phys., 14, 5311-5325, doi:10.5194/acp-14-5311-2014, 2014.
L. Ran, W. L. Lin*, Y. Z. Deji, B. La, P. M. Tsering, X. B. Xu, and W. Wang. Surface gas pollutants in Lhasa, a highland city of Tibet: current levels and pollution implications. Atmos. Chem. Phys., 14, 10721-10730, doi:10.5194/acp-14-10721-2014, 2014.
Lin W., T. Zhu*, Y. Song, H. Zou, M. Tang, X. Tang, and J. Hu, Photolysis of surface O3 and production potential of OH radicals in the atmosphere over the Tibetan Plateau, J. Geophys. Res., 113, D02309, doi:10.1029/2007JD008831, 2008.
W. L. Lin, X. B. Xu*, X. D. Zheng, Jaxi Dawa, Ciren Baima, J. Ma.Two-year measurements of surface ozone at Dangxiong, a remote highland site in the Tibetan Plateau. Journal of Environmental Science, 31C: 133-145, 2015
Tong Zhu*, Weili Lin, Yu Song, Xuhui Cai, Han Zou, Ling Kang, Libo Zhou, and Hajime Akimoto, Downward transport of ozone-rich air near Mt. Everest. Geophysical Research Letters, 33, L23809, doi:10.1029/2006GL027726, 2006.

## Slide 25
Thanks for your patience!

## Slide 26
O3+NO  NO2 +O2

## Slide 27: 拉萨1998夏季vs.2012年夏季

## Slide 28
夏季，地面臭氧浓度受光化学生成和对流混合输送的影响十分显著，午后臭氧可出现4-5小时的高值，特别也出现在一些短暂的高达100-200ppb的过程（几十分钟内）臭氧浓度，观测到O3小时均值可超过160ppb，存在大面积光化学污染的潜势。
highly spatial inhomogeneity in air pollution

## Slide 29: 秋、冬季白天太阳辐射依然强烈，短时的臭氧高值现象出现的频率比夏季更多。这与东部平原地区有显著的差别。