## Slide 1: Airborne Measurements of Ammonia and Implications for Ammonium Nitrate Formation in the Central Valley and the South Coast Air Basin of California
P-3 NH3 Observations
SoCAB NH3 : Cars and Cows
Central Valley Dairy NH3 Flux
NH4NO3 in Central Valley -
  NH3 or HNO3?
J.B. Nowak1,2, J.A. Neuman1,2, R. Bahreini1,2, A. M. Middlebrook2, C.A. Brock2, G. J. Frost1,2, J.S. Holloway1,2, S.A. McKeen1,2, J. Peischl1,2, I.B. Pollack1,2, J.M. Roberts2, T.B. Ryerson2, M. Trainer2, and D.D. Parrish1,2
1CIRES, University of Colorado, Boulder, CO
2NOAA-ESRL, Chemical Sciences Division, Boulder, CO
http://www.esrl.noaa.gov/csd/calnex/
Notes: Focusing on sources in this talk

## Slide 2: California NH3 Area Emissions
EPA NEI 1999v3
(Frost et al., JGR 2006)
All area sources
Point sources excluded
4 km resolution
Grid emissions < 0.05 tons/day not shown
SoCAB
  Agriculture
  Cars
Central Valley
  Agriculture

## Slide 3: P-3 NH3 CIMS Instrument
Chemical Ionization Mass Spectrometry (CIMS) uses ion-molecule reactions to selectively react gas-phase species of interest to an easily detectable product ion. (Nowak et al., JGR, 2007, 2010)
(C3H6O)2H+ + NH3  (C3H6O)2H+NH3
Sensitivity ~ 1± 0.5 Hz/pptv (for 1 MHz reagent ion)
Background ~ 0.2 to 1 ppbv (varied flight-to-flight)
Time Response ~ 1 s
Uncertainty ~ ± (30% + (0.100 to 0.200) ppbv)

## Slide 4: P-3 NH3 Sampling Strategy
Dairy locations from Salas et al., PIER Report, 2008
Flight tracks
  May 7 – SJV
  May 14 – LA
6 flights in the Central Valley
7 flights through the SoCAB
Notes: Salas,␣William,␣Li,␣Changsheng,␣Mitloehner,␣Frank,␣and␣John␣Pisano.␣2008.␣Developing␣and␣ Applying␣Process␣Based␣Models␣for␣Estimating␣Greenhouse␣Gas␣and␣Air␣Emission␣From␣California␣ Dairies.␣California␣Energy␣Commission,␣PIER␣Energy␣Related␣Environmental␣Research.␣CEC␣ 500␣2008␣093␣
PIER – Public Interest Energy Research

## Slide 5: High NH3 Mixing Ratios
May 7 - 963 ppbv
May 14 - 140 ppbv
Peak Mixing Ratios
Notes: Hot Spots also seen from Satellites, IASI NH3 Nature Geoscience 2009.

## Slide 6: CalNex NH3 Altitude Profile
  NEAQS 2004
BL mixing ratios up to 3 ppbv
Biomass burning layers at altitude
(Nowak et al., JGR 2007)
  TexAQS 2006
BL mixing ratios up to 8 ppbv
BL plumes from industrial accident
(Nowak et al., JGR 2010)
100 pptv – ~ 1 ppmv
Highest near surface
First in-situ profiles concurrent with satellite observations
Notes: X axis, linear 0-90, logarithmic 100 -1000, begun collaborations with TES and IASI measurement teams

## Slide 7: South Coast Air Basin NH3 Sources
May 14 flight track colored and sized by NH3 mixing ratio
Automobiles
Dairy farms
Notes: Note color scale values and wind

## Slide 8: Why do automobiles emit NH3?
Unregulated byproduct of three-way catalytic converters
  Resulting from over-reduction of NO on the catalyst surface
  Emissions mode dependent (i.e., acceleration events)
Emissions dominated by ‘middle-aged’ vehicles
  Older vehicles - no converter or deactivated catalyst
  Newer vehicles - better process control technology
Now
Mainly light-duty vehicles
Future/Now
SCRs using urea
in heavy-duty vehicles ?
Notes: The production of NH3 emissions is contingent upon the vehicle’s ability to produce NO in the presence of a catalytic convertor that has enough stored hydrogen to reduce the NO to NH3. Dynamometer studies have shown that these conditions are met during acceleration events, particularly when the catalyst surface is slightly fuel rich from a recent deceleration

## Slide 9: NH3 Automobile Source – Data Selection
May 14
NH3:CO
NHx (NH3 + NH4+):CO
Fuel-based NH3:CO
  West LA ~ 0.060
  Fresno ~ 0.040
  San Jose ~ 0.048
Bishop et al., ES&T 2010
2008
May 8, 14, 16, 19, and June 20
Notes: Point out location of Bishop west LA Sampling Location, mol/mol

## Slide 10: NH3 Automobile Source
Summary of May 14 NH3:CO and NHx:CO Ratios |  | 
Transect | NH3:CO | NHx:CO
Red | s = 0.024, r2 = 0.72 | s = 0.031, r2 = 0.81
Blue | s = 0.032, r2 = 0.82 | s = 0.038, r2 = 0.89
Green | s = 0.031, r2 = 0.80 | s = 0.037, r2 = 0.75
Notes: Point out NH3 from dairy, no CO correlations,

## Slide 11: NH3 Automobile Source
NHx:CO within factor of two of Bishop, 2010
2010 estimated SoCAB CO emissions ~ 2.68 x 109 g/day
(www.arb.ca.gov/app/emsinv/emssumcat.php)
For May 14, 83 – 101 metric tons/day
All CalNex, 67 – 101 metric tons/day
Compare to NH3 flux from SoCAB dairy farms
Notes: Calculate with Bishop and 2008 Carb data ~ 115 metric tonnes/day
Estimated 2010 CO emissions published in 2009, average for CalNex 78 metric tonnes/day

## Slide 12: Dairy Farm NH3 Mass Flux Calculation
May 14
  Dairy farm flux ~ 115 metric tons/day (± 50%)
fluxm =vcos(α)• ∫n(z)dz• ∫ Xm(y)dy
Standard method, White et al., Science, 1976
Wind speed
Aircraft track correction
Atmospheric number density over the boundary layer height
Integral of the observed plume
Factor of 2 uncertainty
Two crosswind transects
May 16
  Dairy farm flux ~ 33 metric tons/day (± 50%)

## Slide 13: SoCAB NH3 Sources
May 14 ~ 83 – 101 (metric tons/day) ~ 115 (metric tons/day)
May 16 ~ 61 – 65 (metric tons/day) ~ 33 (metric tons/day)
Cars ≅ Cows
(within factor 2)
Cows geographically concentrated higher mixing ratios

## Slide 14: Consequence of NH3 emissions - NH4NO3
NH4NO3 Formation

## Slide 15: Consequence of NH3 emissions - NH4NO3
NH3 and HNO3 anti-correlated
NO3- increased indicating NH4NO3 formed
~10x more NO3- than in car transects
Notes: NO3 peak ~11 ug m-3
Temp 19 to 16 C, RH 50 to 20%

## Slide 16: Central Valley NH3 Dairy Farm Flux
Estimate flux from dairy farms
Notes: 7th – Southern SJV
11th – Sacramento, Rice
12th – Northern SJV

## Slide 17: Central Valley NH3 Dairy Farm Flux
Same flux calculation
636 metric tons/day
~6-20 times greater than SoCAB dairies
Higher density of cows
Notes: Winds lighter than in SoCAB, ~ 3 m/s compared to 6 m/s.

## Slide 18: Central Valley NH3 Observations
May 7, 11, 12
NH3 peaks at 963 ppbv
Notes: 7th – Southern SJV
11th – Sacramento, Rice
12th – Northern SJV

## Slide 19: Central Valley HNO3 Observations
May 7, 11, 12
HNO3 peaks at 3 ppbv
Notes: Point out low spot on 7th with high NH3 and high NO3-
Similar observations from June 14th,16th,18th flights

## Slide 20: Central Valley NO3- Observations
May 7
NO3- peaks at <2 ppbv
Despite abundance of NH3, NO3- loading relatively small due to lack of HNO3
Notes: And summer time conditions HNO3 limiting seen before.
Different from winter, with lots of NO3- due to temperature shifting equilibrium and accumulation.

## Slide 21: Summary
NH3 mixing ratios high frequently over 10 ppbv, plumes up to 963 ppbv
Estimated SoCAB automobile source 67 to 101 metric tons/day
Estimated SoCAB dairy farm flux ~ 33 to 115 metric tons/day
In South Coast Air Basin:
  Automobile ≈ Dairy farm (within factor of 2)
Central Valley dairy farm flux up to 636 metric tons/day
Despite abundance of NH3 in the Central Valley, observed NO3- levels are low due to the lack of HNO3

## Slide 22: The End

## Slide 23: Sources of Ammonia
Fertilizer Application
Cars, Industry
Biomass Burning, Soil Emissions
Animal Husbandry
Notes: Don’t forget Selective catalytic reduction in cars and power plants

## Slide 24: Measurement Techniques
NH3 - Chemical Ionization Mass Spectrometry (CIMS)
HNO3 - Chemical Ionization Mass Spectrometry (CIMS)
Aerosol Composition - Compact Time of Flight Aerosol Mass Spectrometer (C-ToF-AMS)
Aerosol Size Distributions -
    5-Channel Condensation Particle Counter (CPC)
    Ultra-High Sensitivity Aerosol Spectrometer (UHSAS)
    White Light Optical Particle Counter (White Light-OPC)
CO - Vacuum UV Resonance Fluorescence
http://www.esrl.noaa.gov/csd/calnex/
Notes: Don’t dwell~ mention instruments fast time resolution, calibrated, zeroed

## Slide 25: Importance of Ammonia in the Atmosphere
NH3 typically most abundant atmospheric gas-phase base
Water soluble and readily absorbed to surfaces, i.e., vegetation and soil
Often major component of tropospheric aerosol as NH4+
NH3 + HNO3NH4NO3 Ammonium Nitrate
2NH3 + H2SO4(NH4)2SO4 Ammonium Sulfate
NH3 + HClNH4Cl Ammonium Chloride
Notes: Also comes off of surfaces.